## Slide 1: EM-SLAM
Chaojie Feng

## Slide 2: Expectation Maximization Setting
Expectation–maximization (EM) is an iterative method that attempts to find the maximum likelihood estimator of a parameter of a parametric probability distribution

## Slide 3: EM Toy Example
An illustrative example:
Consider temperature contains 24 hours temperature record for a day. We know temperature distribution where represents seasons {spring, summer, fall, winter}. Our measurements are where measures the average temperature of the day. We want to know given our measurement , what is the maximum likelihood of the season ? To simplify, find such that ?
Notation:
is defined as unknown parameter
is defined as hidden variables
is defined as observations

## Slide 4: EM Toy Example
Step 1: initialize season estimate as in
Step 2: E-step: given the mean temperature and estimate season , compute for all possible and find a best estimate for (Q-function)
Step 3: M-step: based on calculated , find season such that:
Step 4: Repeat step 2 and step 3 until certain convergence criteria

## Slide 5: EM-SLAM
We can follow the same idea in previous toy example to build EM-SLAM architecture
In EM-SLAM setting:
  : landmarks
  : Robot’s pose
  : observations

## Slide 6: EM-SLAM Framework
We want to find the best map representation such that
In the E-Step, we want to formulate a function of expectation of log likelihood conditioned on observations:
Assume is time independent and Markov properties:
can be numerically approximated using E-RTS smoother:

## Slide 7: EM-SLAM Framework
denotes up to all measurement to time
With an E-RTS smoother, we can have and
In the M-Step, we want to solve use L-BFGS Hessian update
Repeat until convergence
Note this is a BATCH algorithm, is iteration number, and we will need all observations to perform computation of for each iteration

## Slide 8: Obtaining Initial Guess
Personally, I think this is the most important part in this paper in terms of implementation
EM is susceptible to local minimum if we have a bad initialization
What is a “bad” initialization ?
In EM-SLAM setting, any orientation with uncertainty is a bad initialization
Thus, the process noise for orientation needs to be set to 0

## Slide 9: Obtaining initial Guess
Assume :
If , and still follows gaussian
However, if is not linear, i.e. , , no longer follows gaussian
As a result, it will have similar problem just like EKF-SLAM

## Slide 10: Why we use EM-slam?
It is impractical in reality because it is an batch algorithm
We still need it because of EM framework on saving computation efficiency:
  EM-SLAM approximately scales linearly to batch length and landmarks: complexity (FOR EACH ITERATION)
  EKF-SLAM approximately scales quadratically in number of landmarks: complexity [1]
  Graph-SLAM and NLS approximately scales quadratically in number of landmarks: complexity [2]
It can be modified for recursive version to make it an online algorithm
  [1] : http://ais.informatik.uni-freiburg.de/teaching/ws12/mapping/pdf/slam08-kf-wrapup.pdf
  [2]: Sjanic, Zoran et al. "EM-SLAM With Inertial/Visual Applications".